## Slide 1: Local AI for historical research
Speed, capacity and source fidelity
8 September 2026
EVO X3 / WINDOWS + INTEL ARC
Notes: Six slides including the cover. Results describe observed configurations and a small source-bound pilot, not a general model ranking. The selected Simple Light Mode template is retained through duplicated native slides.
Sources:
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MODERN-MODELS.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/evo/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/arc-history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/power-profiles/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MAC-HANDOFF.md

## Slide 2: Speed and model capacity
Evo X3
Ryzen AI MAX+ 395 · Radeon 8060S Ubuntu 26.04 · Vulkan
96 GiB reserved for the integrated GPU. Shared memory architecture; not discrete VRAM.
GPT-OSS 120B ran with 63.39 GB weights.
Original baseline: balanced. Current daily profile: performance.
Windows laptop + external Arc
Ryzen AI 9 365 · about 16 GB system RAM Arc Pro B70 · 32 GB discrete VRAM · SYCL
Intel Thunderbolt 5 / USB4 dock detected. Negotiated link bandwidth was not measured.
Internal RTX 5060 Laptop: 8 GB VRAM.
GPT-OSS 120B was not tested on Arc.
Notes: Do not add the Evo GPU reservation and CPU-visible RAM as independent physical memory pools. The Evo has approximately 30.47 GiB CPU-visible memory after the 96 GiB GPU reservation. Different memory architectures and software stacks prevent a simple memory-for-memory comparison. The Windows machine used AC power. The detected dock is not proof of negotiated bandwidth.
Sources:
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MODERN-MODELS.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/evo/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/arc-history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/power-profiles/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MAC-HANDOFF.md

## Slide 3: Arc is faster in the shared synthetic tests
Generation at 2,048-token depth; 256 generated tokens; five repeats.
llama-bench b10852, full GPU offload, F16 cache, flash attention. Reasoning and MTP off.
Model / tested weight family | Evo tokens/s | Arc tokens/s | Comparability
Qwen3 8B · official Q4_K_M | 40.90 | 72.84 | Strongest match: identical GGUF hash
Qwen3.6 35B-A3B · UD Q4 | 59.60 | 71.53 | Artifacts differ; MTP disabled here
Gemma 4 26B-A4B · Q4 | 47.37 | 56.68 | Different quantizers
Qwen3.8 27B · Q4 | 12.58 | 20.42 | Different artifacts / quantization
GPT-OSS 120B · MXFP4 | 52.59 | Not run | Evo capacity result; no Arc comparison
Notes: Rates are mean tg256 at depth2048, not prose accuracy or end-to-end throughput. Qwen8 identical official GGUF is the closest hardware comparison; operating systems/backends still differ. Evo Qwen35 here is the UD artifact used in the audit. A separate installed community Qwen35 reached 69.43 tokens/s, so 59.60 is not the fastest installed Evo result. Internal RTX5060 Qwen8 was 62.01 tokens/s. These additional configurations are not silently substituted. The optional Arc Nemotron49B capacity test is outside this table. Evo original baseline was balanced.
Sources:
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MODERN-MODELS.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/evo/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/arc-history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/power-profiles/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MAC-HANDOFF.md

## Slide 4: History timings include different kinds of waiting
Twelve requests each; loading excluded. Qwen / Gemma reasoning OFF; GPT-OSS template medium.
Evo: visible-phase rates. Arc: server decode rates. Rate definitions differ; do not pool them.
System / model | Rate: tokens/s | Rate basis | First visible: seconds | Total: seconds
Evo · Qwen35, MTP on | 61.65–95.96 | Visible phase range | 3.69–18.04 range | 140.96
Evo · Gemma26 | 42.54–46.63 | Visible phase range | 4.38–17.29 range | 192.52
Evo · GPT-OSS120 | 44.70–49.19 | Visible phase range | 9.87–78.50 range | 427.84
Arc · Qwen35, MTP off | 68.39 | Weighted decode | 4.89 median | 139.00
Arc · Gemma26 | 52.20 | Weighted decode | 4.08 median | 156.11
Arc · Qwen27 | 19.94 | Weighted decode | 12.71 median | 490.35
Notes: Evo native LM Studio SDK retokenized visible output. Its visible phase excludes initial waiting but includes final overhead. Arc completion-token counts divided by summed server prediction time include any control tokens in that counter and exclude prompt processing. Evo GPT used template-medium reasoning, generated 9,124 reasoning tokens, and had unsupported native top-k and reasoning fields omitted after preflight. Qwen35 MTP was on for Evo history and off for Arc. Gemma and Qwen artifacts differ across machines. Qwen35 Evo fastest merge output was an exact whitespace-normalized concatenation of direct summaries. Total wall times cover different outputs and lengths, so they are not an isolated hardware comparison. Only one battery per configuration.
Sources:
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MODERN-MODELS.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/evo/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/arc-history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/power-profiles/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MAC-HANDOFF.md

## Slide 5: Strong extraction coexists with summary errors
Twenty questions include four true absences. All configurations answered those four correctly.
This secondary content crosswalk uses Evo conventions; stricter Arc completeness scores differ.
System / model | Supported / 20 | Partial | Other answer issue | Summary finding
Evo · Qwen35 | 19 | 1 | None in this category | Wrong reunifier; merge copies summaries
Evo · Gemma26 | 18 | 2 | None in this category | Full-source control omits two passages
Evo · GPT-OSS120 | 19 | 0 | 1 false abstention | Kinship, cause and location errors propagate
Arc · Qwen35 | 19 | 1 | Duplicated answer ID | Wrong reunifier; merge omits H4
Arc · Gemma26 | 18 | 1 | 1 false-absence claim | Reunification / cession conflation
Arc · Qwen27 | 19 | 1 | None in this category | Wrong seller; full-source omits H4
Notes: Small source-bound, Codex/AI-assisted audit, not independent human adjudication or a general accuracy ranking. Four answerable source passages from Charles Oman, The Byzantine Empire. Seventeen fixture hashes were frozen before held-out generation. Partial answers receive no arbitrary half-credit. Arc initial strict completeness counts were Qwen35 16, Gemma16, Qwen27 19. The secondary published crosswalk yields the table shown. ¹Arc Qwen35 repeats H1-Q4; content mapping identifies H1-Q5, while strict ID matching subtracts one supported answer. ²Arc Gemma gives a correct second component but falsely claims Romanus removal is absent; this category differs from Evo GPT declining the whole answer. No claim that Gemma is generally error-free: the original full-book audit found material errors. All six configurations have summary defects. Citation, quotation, coverage and word-limit audits remain separate.
Sources:
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MODERN-MODELS.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/evo/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/arc-history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/power-profiles/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MAC-HANDOFF.md

## Slide 6: Model choices for historical work
Performance mode is saved. Paired checks found no meaningful speed gain.
Daily Evo
Evo fits GPT-OSS120. This pilot established no general quality advantage.
Larger models
Check claims, qualifiers, citations and coverage separately from speed.
Source fidelity
Published handoff covers capacity, >40 tokens/s and the shared accuracy suite.
Mac replication
Start with Qwen35
It combined useful speed with strong extraction content in this pilot.
Every configuration still needs source checks for summaries.
The Mac comparison should preserve frozen prompts and report its own weight hashes.
Notes: The performance profile was explicitly requested after the reversible comparison and is saved in power-profiles-daemon state; daemon active and enabled. No reboot test was performed. Two-model paired profile comparison had small n, fixed order and no randomized crossover; it does not establish a causal thermal or performance effect. Qwen prose mean changed −1.19%, Gemma +0.63%. Speed alone cannot justify summary trust. Mac hardware is user-reported M5 Pro 48GB and should be verified by the running Mac task. Do not claim Mac results or that the Mac task has read the handoff. Handoff asks to avoid duplicate GPU runs and choose the largest practical historical-research capacity candidate with memory headroom.
Sources:
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MODERN-MODELS.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/evo/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/arc-history-v2/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/results/2026-09-08/power-profiles/README.md
https://github.com/MorarFS/hardware-benchmarks/blob/5a99a555753f61f51a50c2089a06831a8b675349/MAC-HANDOFF.md